Steps to Performing an Energy Audit

- Meet with representatives of every area that is to be included in the audit to discuss and list the energy-intensive systems and equipment in those areas, including:

  - The locations of the systems/equipment (Refer to available maintenance or finance lists, information from utility bills, or walk through the building itself.)

  - A practical sequence for touring these areas

  - Whether “after hours” tour might be worthwhile (particularly for areas that include compressed air or other systems in which audible leaks may occur)

  - How long it will take to tour each area

  - Whether you have the expertise to conduct the audit successfully, or if professional assistance may be necessary for at least some of the audit effort

- Plan the audit:

  - Create a checklist for use during the tour, starting with the provided tool, “Sample Walk-through Guide and Observations Checklists.”

  - Choose individuals to participate in the audit tour, preferably those who are familiar with the equipment and processes.

  - If professional help is needed, coordinate with them.

  - Identify the equipment needed during the tour, starting with the provided tool “Energy Audit Supplies.”

  - Set a schedule and notify all participants.

  - Ensure that all participants understand what to look for during the audit tour:

    - Power running unnecessarily

    - Needed repairs and maintenance

    - Unnecessary uses of energy

    - ??

- Conduct the audit tour, using:

  - A version of the provided tool “Audit Report Template” on which to write your audit notes

  - The provided tool “Tips for the Audit Tour” as a guide for all participants

  - Your prepared checklist

  - The assembled energy audit supplies

- Review the findings of the audit with all those who participated and discuss:

  - The types of energy waste observed

  - Opportunities for energy savings

  - Subjects for which more data would be helpful

  - Causes of any waste and ideas for eliminating them

  - Energy projects that would address these issues, which you should record and prioritize on a “Potential Projects Technical Priority Worksheet”